## Slide 1: Perpetual Environmentally Powered Sensor Networks

## Slide 2: Introduction
Prometheus
[prəˋmiθjəs]
【希神】普羅米修斯

## Slide 3: Introduction
Scenario :
  Operating at low duty cycles.
  Unpredictable environment.
  System should adapt to available energy reserve.

## Slide 4: Introduction
Problems:
  Physical deterioration of the energy storage device.
  Ex: Rechargeable batteries have about 300 to 500 recharge cycles.
Challenge:
  Reducing the stain on storage element while preserving simple hardware and software architecture.

## Slide 5: Architecture
Notes: Primary buffer is super capacitor
Use MCU to do power management

## Slide 6: Power Management Policy
The supercapacitor must provide energy to consumer most of the time.
Minimize access to the secondary buffer to prolong its lifetime.

## Slide 7: Solar Panel
The size of the solar panel should be determined based on how fast the primary buffer should be replenished.
Larger solar cells only yield quicker charging.

## Slide 8: Wireless Sensor Node
The sensor node influences the system’s power consumption by changing its duty cycle.
D is chosen by the application.
if the application knows the energy levels of the two buffers, it can adjust duty cycle intelligently.
Ex: this information can be shared across nodes to make routing decisions.

## Slide 9: Primary Buffer: Supercapacitor
Advantages:
  Virtual infinite charge cycles
  Ideal for frequent pulsing application
    Volatile input and frequent charge cycles.
  Without time deterioration
Drawbacks:
  Higher leakage current
  Larger size
  Cost

## Slide 10: Primary Buffer: Supercapacitor
Primary buffer supercapcitor should be as large as possible to prolong lifetime.
The larger the capacity, the larger the leakage current.

## Slide 11: Primary Buffer: Supercapacitor
Configuration to reduce leakage.
Leakage is proportional to energy level.
=>Lower by wiring two supercapacitors:

## Slide 12: Secondary Buffer: Lithium Battery
When the primary exhausted, the secondary buffer is used.
hold energy for a long period of time.
low leakage but not charged or discharged frequently.

## Slide 13: Software compensation
This may trigger a charge when not necessary.
Use software make compensated readings for true battery capacity.

## Slide 14: Sensing and Control
Application with an active period at least once an hour is sufficient
Internal reference voltages of Telos are only 2.5V 1.5V => use 1M ohms resistor as divider instead of 1k ohms resistor
Notes: 1M 誤差雖大 但功耗少

## Slide 15: Charging Circuit & Driver
Software control all the power management.
Shallow discharge/charge can extend the battery’s life.
Notes: 充電的方法很多 可以純硬體 也可以軟應配合 也可純軟 選純軟最簡單 省電 又能執行複雜的scheme

## Slide 16: Example: Dynamical Duty Cycle
Dynamically adjust duty cycle based on energy in the primary buffer.

## Slide 17: Result & Analysis(Scenario 1)
Conditions:
  Reference voltage changing
  1% duty cycle
  During the night and energy in supercap is low
Reference voltage
  2.5v -> 1.5v -> 2.5v

## Slide 18: Result & Analysis(Scenario 2)
Initiation of charging
1% duty cycle
During sunrise
Start with low battery level
Charging start

## Slide 19: Result & Analysis
No light condition with 200mAh battery:

## Slide 20: Conclusion

## Slide 21: END
Thanks for your attention!