## Slide 1: System Architecture Direction for Networked Sensors
Group 4
499415130 601415010 601441045
王維寬 林奕丞 鄭賜福
Jason Hill, Robert Szewczyk, Alec Woo,
Seth Hollar, David Culler, Kristofer Pister
Department of Electrical Engineering and Computer Sciences
University of California, Berkeley

## Slide 2: Outline
Introduction
Network Sensor Characteristics
Example Design Point
Tiny Microthreading Operating System (TinyOS)
Evaluation
Related Work
Architectural Implications

## Slide 3: Outline
Introduction
Network Sensor Characteristics
Example Design Point
Tiny Microthreading Operating System (TinyOS)
Evaluation
Related Work
Architectural Implications

## Slide 4: What enables the networked sensor?
4 important trends:
  Moore’ s law
  Systems on a chip
  Integrated low-power communication
  Integrated low-power transducers

## Slide 5: Two issues for the design regime
Concurrency intensive
  Several flows of data must be kept moving simultaneously.
Efficient modularity
  Hardware specific and application specific components must snap together with little processing and storage overhead.

## Slide 6: Following topics
Section 2 :
  Design requirement and microthreading approach
Section 3 :
  Current-technology hardware design
Section 4 :
  Development of TinyOS
Section 5 :
  Evaluation of the effectiveness
Section 6 :
  Contrast with other embedded operating system
Section 7 :
  Implication for the architectural directions

## Slide 7: Outline
Introduction
Network Sensor Characteristics
Example Design Point
Tiny Microthreading Operating System (TinyOS)
Evaluation
Related Work
Architectural Implications

## Slide 8: Design requirements
Small physical size and low power consumption :
  Size and power constrain the processing, storage and interconnect capability.
Concurrency-intensive operation :
  The primary mode of operation : Flow information.
Limited physical parallelism and controller hierarchy :
  Capabilities and sophistication of the controller are much lower than conventional systems.
Diversity in design and usage :
  Networked sensor devices tend to be application specific.
Robust operation :
  These devices are unattended and operated in long time.

## Slide 9: Outline
Introduction
Network Sensor Characteristics
Example Design Point
Tiny Microthreading Operating System (TinyOS)
Evaluation
Related Work
Architectural Implications

## Slide 10: Hardware configuration

## Slide 11: Hardware organization
Processor :
  Using the MCU - ATMEL AT90LS8535.
  8-bit Harvard architecture with 16-bit addresses.
  32 8-bit general registers.
  Processing at 4 MHz.
  Operating voltage 3 V.
  8 KB of flash and 512 bytes of SRAM. <-- The memory is very constrained !!
  3 sleep modes : idle, power down and power save.
LEDs :
  3 LEDs are connected through general I/O ports.
Photo sensor :
  Connected through ADC.
Radio :
  An RF Monolithics 916.50 MHz transceiver ( TR1000 ) .
Temperature sensor :
  Analog devices - AD7428.
Serial port - UART:
  Transmit mode : taking a byte of data and shifting it out.
  Receive mode : sampling the input pin and shifting in bits.
Coprocessor :
  Using the MCU - ATMEL AT90LS2343
  Reprogramming the main microcontroller.

## Slide 12: Power characteristics
Table 1 :
  Powered by an Energizer CR2450 lithium battery
2 configurations :
  Mobile sensor
    Temperature and light reading
    Limited energy
  Stationary sensor
    Bridging the radio network
    Having power supplied.

## Slide 13: Outline
Introduction
Network Sensor Characteristics
Example Design Point
Tiny Microthreading Operating System (TinyOS)
Evaluation
Related Work
Architectural Implications

## Slide 14: 4 Component parts
A set of fixed-size frame
Event handler
A Bundle of simple task
Command handler

## Slide 15: A set of fixed-size frame
It prevents the overhead associated with dynamic allocation.
Execution time savings because variable locations can be statically compiled into the program instead of accessing thread state via pointers.

## Slide 16: Event handler
The lowest level components have handlers connected directly to hardware interrupts
An event handler can deposit information into its frame, post tasks, signal higher level events or call lower level commands

## Slide 17: Command
A command will deposit request parameters into its frame and conditionally post a task for later execution.
A command must provide feedback to its caller by returning status indicating whether it was successful or not.

## Slide 18: Task
Tasks allow us to simulate concurrency within each component, since they execute asynchronously with respect to events.
FIFO scheduler.
Our prototype puts the processor to sleep when the task queue is empty.

## Slide 19: Component types
Hardware abstraction
Synthetic hardware
The high level software components

## Slide 21: A sample messaging component

## Slide 22: Put it together
Each sensor can act as a router for packets traveling from sensors that are out of range of the base station.
Each device must respond to : the arrival if a rout update, the arrival of a message that needs to be forwarded, the collection of new data

## Slide 24: Outline
Introduction
Network Sensor Characteristics
Example Design Point
Tiny Microthreading Operating System (TinyOS)
Evaluation
Related Work
Architectural Implications

## Slide 25: Evaluation
Small physical size
Concurrency-intensive operation
Efficient modularity
Limited physical parallelism and controller hierarchy
Diversity in usage and robust operation

## Slide 26
Small physical size:
  Table 2 shows the code and data size

## Slide 27
Concurrency-intensive operation:
  important baseline characteristic -> context switch speed
  Table 3 shows intrinsic hardware cost for moving bytes in memory.

## Slide 28
Step 0 : Starting from the hardware timer interrupt
Step 1 : Events propagate up through the TX_bit_evt into byte-level processing.
Step 2 : Handler issues a command to transmit the final bit and then fires the
TX_byte_ready event to signal the end of the byte.
Step 3 : Trigger TX_packet_done
Step 4 : Signal the application that the send_msg command has finished
Step 5 : Issues another asynchronous send_msg command
Step 6 : Post a task at to send the packet.
Efficient modularity:
  Events and commands can propagate through components quickly.

## Slide 29
Limited physical parallelism and controller hierarchy:
  The processor is idle approximately 50% of the time in highly active period and the remaining time used to access other sensors.
  Implement bit level functions on a separate microcontroller incur :
(a)can’t realize a performance gain because of the radio
bandwidth limitations.
(b)additional power and time expense in transferring
data between microcontrollers.
Diversity in usage and robust operation
  The versatility of the architecture .
  Target multiple CPU architectures in C.
  When one node failure, routing application automatically reconfigures itself.

## Slide 30: Outline
Introduction
Network Sensor Characteristics
Example Design Point
Tiny Microthreading Operating System (TinyOS)
Evaluation
Related Work
Architectural Implications

## Slide 31: Related Work
Developing microelectromechanical sensors and new communication devices make a strong case for the development of a software platform to support and connect them.
  EX: TinyOS
Traditional real time embedded operating systems :

## Slide 32
Finite state machine (FSM) description language :
  express component designs that are compiled down to software.
Device side :
  Cubic millimeter sensor.
  Low power hardware.
  Efficient software .

## Slide 33: Outline
Introduction
Network Sensor Characteristics
Example Design Point
Tiny Microthreading Operating System (TinyOS)
Evaluation
Related Work
Architectural Implications

## Slide 34: Major design question
Whether or not individual microcontrollers should be used to manage each I/O device?
  The tradeoffs :
    Power consumption.
    Speed of off chip communication.
    Flexibility and functionality.
  Using a higher performance ARM Thumb.
    Won’t change the architecture.

## Slide 35: Impact of changing architecture
The inclusion of hardware support for events would make significant performance impact.
  An additional register set for event execution would save about 20 μs per event or 20 % of total CPU load.
The result shows the hardware support for radio collection would save about 690 μ J per bit in processor overhead.
  This represents the elimination of bit level processing from the CPU.

## Slide 36: Reconfigurable
The traditional system is configured for a particular system niche.
Reconfigurable computing has the potential of making WSN highly versatile.
For example : the Radio Byte
  it consumes a significant amount of CPU time and must be radio protocol specific.

## Slide 37: End
Thanks for your attentions.