## Slide 1: Simulation Tools for Wireless Sensor Networks
Group 4
499415130 601415010 601441045
王維寬 林奕丞 鄭賜福
E. Egea-López, J. Vales-Alonso, A. S. Martínez-Sala,
P. Pavón-Marińo, J. García-Haro
Department of Information Technologies and Communications
Polytechnic University of Cartagena, Spain

## Slide 2: Outline
Introduction
A model for WSN simulation
Framework selection
WSN simulation software
Conclusions and open issues

## Slide 3: Outline
Introduction
A model for WSN simulation
Framework selection
WSN simulation software
Conclusions and open issues

## Slide 4: Introduction
Wireless Sensor Networks (WSN) can be considered a particular type of Mobile Ad-hoc network (MANETs),
WSNs and MANETs share similar technical
problems.
There are two specific factors in WSN: (a)network traffic
(b)energy
Deploying and operating a testbed

## Slide 5
There are two key to obtain reliable conclusions
(a) The correctness of the model.
(b) the suitability of a particular tool to implement
the model.
the methodology and assumptions of simulations can lead to mistaken results.
─ Idealized hardware
─ protocols
─ non realistic radio model

## Slide 6: Outline
Introduction
A model for WSN simulation
Framework selection
WSN simulation software
Conclusions and open issues

## Slide 7: A MODEL FOR WSN SIMULATION
WSN simulation tools
(a) Network model
-node
-Environment
-Radio channel:
-Sink nodes
-Agents
(b) Node model
-Protocol tier
-physical-node tier
-media tier

## Slide 9: Network model
Node:
─ a physical device monitoring a set of physical
variables.
─ communicate via a common radio channel.
─ sensor modes is connected to environment.
─ WSN can contain from a few to several
thousands of nodes.

## Slide 10
Environment:
─ environment component
(1)generation and propagation of events that
are sensed by the nodes
(2)trigger sensor actions
Radio channel:
─ Very detailed modelsuse a “terrain” component
Sink nodes:
─ receive data from the net
─ process data
Agents:
─ A generator of events of interest for the nodes.

## Slide 11: Node model

## Slide 12
Protocol tier
(1) Comprises all the communication protocols.
(2) Three layers coexist at this tier:
─MAC layer
─ routing layer
─specific application layer.
(3) Depends on the state of the physical tier

## Slide 13
Physical-node tier
(1)common elements
─ Set of physical sensors:
Describe the behavior of the monitoring
hardware
─ Energy module:
Simulates power consumption in the
component hardware
─ Mobility module:
Controls sensor position.

## Slide 14
Media tier
(1) the link of the node with the “real world”
(2) connected with the environment through
─ radio channel
─ physical channel

## Slide 15: Outline
Introduction
A model for WSN simulation
Framework selection
WSN simulation software
Conclusions and open issues

## Slide 16: FRAMEWORK SELECTION
Existing WNS frameworks can be categorized In:
(1) Specific add-ons to general purpose
communication networks
(2) WSN frameworks built from scratch.
The long-way road to simulation
What may we expect from a good WSN simulator?

## Slide 17
The long-way road to simulation
a simulation framework:
(a)smulation library
─ set of software libraries in a high level
programming language
(b)utility library
─graphical representation support
─statistical data gathering and analysis
(c)some scripting
─Tcl
─XML

## Slide 18
What may we expect from a good WSN simulator?
─ Reusability and availability.
─ Performance and scalability.
─ Support for rich-semantics scripting languages
to define experiments and process results.
─ Graphical, debug and trace support.

## Slide 19
Reusability and availability:
(1) implementation of common models
─ Early and widely adopted frameworks are
added to next releases.
(2) modify or integrate a new model with the
existing ones?
─ A careful structure with clean interfaces
and high modularity allows the user to easily
add or change functionality.

## Slide 20
(3) typical requirements for WSN simulators:
─ Ad-hoc routing support plus wireless MAC
protocols
─ propagation and mobility models to synthesize
the physical node distribution
(4) All the specific frameworks are able to execute
native sensor code.

## Slide 21
Performance and scalability:
(1) bounded to the programming language
effectiveness
(2) constrained to the memory, processor and
logs storage size requirements.
(3) type of simulation limit:
─ operate real time cannot be arbitrarily
long.

## Slide 22
Support for rich-semantics scripting languages
to define experiments and process results.
(1) input scripting languages
─ high level semantics.
(2) output scripting language
─ obtain the results from the experiments
quickly

## Slide 23
Graphical, debug and trace support.
(1) As a debugging aid
─ quickly detect a bad behavior is to “watch”
and follow the execution of a simulation.
(2) As a visual modeling and composition tool
─ facilitates and speeds the design of small
experiments
(3) as result plotters

## Slide 24: Outline
Introduction
A model for WSN simulation
Framework selection
WSN simulation software
Conclusions and open issues

## Slide 25: WSN simulation software
In this section, we focus on free, open-source, simulation tools.
Two kinds of simulation software :
  General simulation packages
  Specific WSN frameworks

## Slide 26: General simulation packages
In this section, we focus on free, open-source, simulation tools.
Two kinds of simulation software :
  General simulation packages
  Specific WSN frameworks

## Slide 27: General simulation packages
NS-2
  A discrete event simulator
  Developed in C++
  Advantages :
    Most complete protocol models
    Network up to 1000 nodes
  Disadvantage :
    Poor graphical support

## Slide 28: General simulation packages
OMNET++
  A discrete event simulator
  Developed in C++
  Advantages :
    It’s simple due to its clean design
    Powerful GUI library
  Disadvantage :
    Lack of available protocols

## Slide 29: General simulation packages
J-Sim
  Component-based simulator
  Developed in Java
  Advantages :
    Considerable protocols
    Reusable and interchangeable model
    Provide GUI library
  Disadvantage :
    A 41 % worse execute time than NS-2

## Slide 30: General simulation packages
NCTUns2.0
  A discrete event simulator
  Developed in Unix machine
  Advantages :
    Can be fed with real program data sources
    High number of protocols
    Worthy graphical edition capabilities
  Disadvantage :
    No specific designs for WSN
    Hard to be available in Linux machine

## Slide 31: General simulation packages
JiST / SWANS
  A discrete event simulator
  Developed in Java byte-code
  Advantages :
    Claim to scale to network of 106 nodes
    Better event throughput and memory consumption
  Disadvantage :
    Lack of enough protocol models
    Only provide ad-hoc network

## Slide 32: General simulation packages
GloMoSim
  A simulation environment
  Built with Parsec :
    A language derived from C
  Scale to 10,000 nodes
SSFNet
  Set of Java network models
  Built over the SSF
    A specification of a common API for simulation
  Simulation of very large scale networks

## Slide 33: General simulation packages
Ptolemy II
  A Java packages that support different models
  Has simple and intuitive graphical composition

## Slide 34: Specific WSN framework
TOSSIM
  A discrete event simulator
  Emulator of TinyOS with nesC code
  Handle around a thousand of motes
  Goal :
    Study the behavior of TinyOS
  Limitations :
    Not capture energy consumption
    Every node run the same code

## Slide 35: Specific WSN framework
EmStar / EmSim / EmTOS
  Platform : microservers
    Ad-hoc systems with better hardware
  EmTOS :
    An extension of EmStar the enable nesC / TinyOS
  Claim to handle over 500 nodes
ATEMU
  An emulator of the AVR processor
    Use in MICA platform
  Advantages :
    Capability of testing OS and application
    Capability of simulating heterogeneous networks

## Slide 36: Specific WSN framework
SENS
  A discrete event simulator
  Developed in C++
  NesC can be used directly on it
Prowler / JProwler
  A discrete event simulator on MATLAB
  JProwler is the Java version
SNAP
  An integrated hardware platform
  2 way of usages :
    The core of a deployed sensor
    A part of an array of processors

## Slide 37: Outline
Introduction
A model for WSN simulation
Framework selection
WSN simulation software
Conclusions and open issues

## Slide 38: Conclusion and open issues
Simulation is essential due to :
  Unfeasibility of analysis
  Difficulties of setting up real experiments
The lack of protocols increase development time .
The parallel simulations perform better scale than sequential ones .
Bad graphical editors takes much time to create model.
All specific WSN framework is available of native code from actual devices.

## Slide 39: End
Thanks for your attentions.